## Slide 1
TIME SERIES
ANALYSIS & FORCASTING
TEAM - DEEPESH YADAV
VENKAT
Predicting Bengaluru’s Future: NDVI, Rainfall, AQI, Temperature Trends for a Sustainable Tomorrow!

## Slide 2
PROJECT OVERVIEW
    To analyze the relationship between urbanization, vegetation health (NDVI), air quality (AQI), Rainfall and Temperature in Bengaluru, Chennai.
    To develop a predictive model using satellite data (Sentinel-2, Sentinel-5P, MODIS, ERA5) to forecast AQI, NDVI, Rainfall and Temperature in the coming years, thereby supporting sustainability efforts in urban planning and policymaking.
Objective

## Slide 3
Time Series Overview
Time series forecasting is a technique used to predict future values based on previously observed data points collected over time. It involves identifying patterns such as trends, seasonality, and cyclical behaviors to make informed predictions.
A time series consists of:
  Trend: Long-term movement in data.
  Seasonality: Repeating patterns at regular intervals.
  Cyclic Patterns: Irregular fluctuations that are not tied to seasonality.
  Noise: Random variations with no predictable pattern.
What is Time Series Forecasting?

## Slide 4
Data Collection & Preprocessing
  Multi-Source Satellite Data
    NDVI (Vegetation Health): Landsat 8
    Temperature & Rainfall: ERA5-Land, CHIRPS
    Air Quality (NO₂ & Aerosol Index): Sentinel-5P
  Temporal Structure
    Time-series data with daily/monthly timestamps
    Enables trend analysis and forecasting
Data Overview :
  Spatial Structure
    Data extracted for a defined geographical region (e.g., city + 10 km buffer)
  Final Data Format (Tabular)
    Columns: Date, NDVI, Temperature, Rainfall, NO₂, Aerosol Index
    Suitable for EDA, visualization, and predictive modeling

## Slide 5
Data Collection & Preprocessing
Data Overview :

## Slide 6
    Handling Missing Values
    Linear Interpolation used to fill gaps in NDVI, Temperature, Rainfall, NO₂, and Aerosol Index
Data Cleaning & Preprocessing:
Plots:

## Slide 8
  Z-Score Method
    Detects outliers using standard deviation from the mean.
    Values beyond a threshold of 3 standard deviations are considered outliers.
  Handling Low-Variation Columns
    If a column has very low standard deviation, outlier removal is skipped to avoid data distortion.
  Replacement & Interpolation
    Outliers are marked as NaN and filled using linear interpolation to maintain continuity.
  Diagnostic Visualization
    Before & After Scatter Plots are used to confirm effective outlier removal.
Data Cleaning & Preprocessing: (Removing Outliers)

## Slide 9
Visualizations:

## Slide 10
  Rolling Mean (Moving Average)
    Applied to smooth fluctuations and reveal trends
    Helps reduce short-term variations in NDVI, Temperature, Rainfall, NO₂, and Aerosol Index
  Savitzky-Golay Filter
    A polynomial smoothing technique preserving trends
    Reduces noise while maintaining data structure
  Seasonal Trend Decomposition
    Uses rolling statistics to extract long-term trends
    Helps in understanding seasonality effects
Data Cleaning & Preprocessing: (Data Smoothing)

## Slide 11
Visualizations:

## Slide 12
Trend Analysis:
    Rolling Mean (Moving Average): Applied to smooth short-term fluctuations.
    Trend Extraction: Using a centered rolling window to highlight long-term patterns.
    Detrending: Removing the trend component to analyze residual variations.
Seasonality Analysis:
  Seasonal Decomposition: Uses seasonal_decompose to separate trend, seasonal, and residual components.
  Monthly Mean Centering: Identifies repeating seasonal patterns by calculating monthly averages.
Exploratory Data Analysis (EDA)

## Slide 13
Trend & Seasonality Analysis :
(NDVI) -->
  Trend Component (long-term movement)
  Seasonal Component (recurring patterns)
  Residual Component (random noise)

## Slide 14
Trend & Seasonality Analysis :
(Temperature) -->

## Slide 15
Trend & Seasonality Analysis :
(Precipitation) -->

## Slide 16
Distribution & Anomaly Detection
Exploratory Data Analysis (EDA)

## Slide 17
Case Study (why anamolies ?)
Precipitation (Rainfall):
Temperature:
NDVI:
NO2 concentration:
Reference
Reference
Reference
Reference
Reference
then where all vehicles gone after 2019 ?:

## Slide 18
Histogram :
  Shows the frequency distribution of variables (e.g., NDVI, temperature).
  Helps in understanding normal vs. extreme values.

## Slide 19
Box plots to analyse the seasonal variations

## Slide 20
Correlation & Relationships
Exploratory Data Analysis (EDA)
  NDVI & Precipitation → 0.60 (Moderate Positive Correlation)
  🌱 Why? More rainfall usually increases vegetation growth (higher NDVI).
  Precipitation & AQI (NO₂) → -0.42 (Negative Correlation)
  🌧 Why? Rain helps clean pollutants from the air, lowering NO₂ levels.

## Slide 21
Model Development & Forecasting
Traditional vs. Machine Learning Approaches :
  Traditional Approaches: SARIMA/SARIMAX models use historical patterns for forecasting.
  Machine Learning: Random Forest leverages feature engineering and non-linear relationships.
  Hybrid Approach: Combining statistical and ML models can improve accuracy.

## Slide 22
SARIMA Model / Random Forest
Interpretation of Metrics
  RMSE (Lower is Better): Measures the average prediction error in the same unit as the target variable. A lower RMSE means better accuracy.
  R^2 (Closer to 1 is Better): Measures how well the model explains variance in the data. A negative R^2 means the model is worse than a simple mean prediction.

## Slide 23
Visualizations:

## Slide 24
Visualizations:

## Slide 25
Model Training & Validation
Data Splitting:
Training Set: 80%
Testing Set: 20%
Model Training:
Random Forest:
n_estimators=100, random_state=42
SARIMA:
order=(1, 1, 1), seasonal_order=(1, 1, 1, 12)
Model Evaluation:
Predicted values compared to actual test data.
Evaluation Metrics:
Root Mean Squared Error (RMSE): Measures prediction error.
R² Score: Explains model accuracy.

## Slide 26
Dashboard Api

## Slide 27
Prediction api

## Slide 28
    Urban Planning:
      Guide sustainable growth through evidence-based policy.
    Environmental Protection:
      Mitigate air pollution by predicting hazardous levels.
    Public Health:
      Provide real-time information for residents, especially vulnerable groups.
    Climate Change Adaptation:
      Analyze the potential future impacts of climate change on air quality and vegetation.
Impact & Sustainability

## Slide 29
“The project will provide valuable insights for urban sustainability in Bengaluru by forecasting key environmental parameters (AQI(NO2), NDVI, Rainfall & Temperature). The predictive models and will serve as tools for policymakers, urban planners, and the general public to take proactive actions for a healthier, greener Bengaluru.”
Conclusion

## Slide 30
THANK YOU!